## Slide 1: Class 4 Inertia and Responding To Climate Change
Climate Change
OLLI Summer 2013

## Slide 2: Increase in Equilibrium Temperature Due to Increase in CO2 Concentration from 280 ppm
ΔT = ΔT2X * Ln(new CO2 concentration/280 ppm concentration)/Ln(2.0)
Ln(2.0) = 0.69
Current sensitivity estimate:
1.5o to 4.5o

## Slide 3
Chart: CO2 Concentration, Climate Sensitivity And Equilibrium Temperature
| 280 | 290 | 300 | 310 | 320 | 330 | 340 | 350 | 360 | 370 | 380 | 390 | 400 | 410 | 420 | 430 | 440 | 450 | 460 | 470 | 480 | 490 | 500 | 510 | 520 | 530 | 540 | 550 | 560
Ln 1.5 | 0 | 0.075939 | 0.1493 | 0.22026 | 0.28897 | 0.35556 | 0.42016 | 0.48289 | 0.54386 | 0.60315 | 0.66086 | 0.71707 | 0.77186 | 0.8253 | 0.87744 | 0.92836 | 0.97812 | 1.0267 | 1.0743 | 1.1209 | 1.1664 | 1.211 | 1.2548 | 1.2976 | 1.3396 | 1.3808 | 1.4213 | 1.461 | 1.5
Ln 4.5 | 0 | 0.22782 | 0.44791 | 0.66079 | 0.8669 | 1.0667 | 1.2605 | 1.4487 | 1.6316 | 1.8094 | 1.9826 | 2.1512 | 2.3156 | 2.4759 | 2.6323 | 2.7851 | 2.9343 | 3.0802 | 3.2229 | 3.3626 | 3.4992 | 3.6331 | 3.7643 | 3.8928 | 4.0189 | 4.1425 | 4.2639 | 4.383 | 4.5
Linear 1.5 | 0 | 0.075939 | 0.15188 | 0.22782 | 0.30376 | 0.3797 | 0.45563 | 0.53157 | 0.60751 | 0.68345 | 0.75939 | 0.83533 | 0.91127 | 0.98721 | 1.0631 | 1.1391 | 1.215 | 1.291 | 1.3669 | 1.4428 | 1.5188 | 1.5947 | 1.6707 | 1.7466 | 1.8225 | 1.8985 | 1.9744 | 2.0504 | 2.1263
Linear 4.5 | 0 | 0.22782 | 0.45563 | 0.68345 | 0.91127 | 1.1391 | 1.3669 | 1.5947 | 1.8225 | 2.0504 | 2.2782 | 2.506 | 2.7338 | 2.9616 | 3.1894 | 3.4173 | 3.6451 | 3.8729 | 4.1007 | 4.3285 | 4.5563 | 4.7842 | 5.012 | 5.2398 | 5.4676 | 5.6954 | 5.9233 | 6.1511 | 6.3789
Notes: OLLI summer 2013 class 3 workpaper

## Slide 4: 2007 IPCC CO2 Scenario Projections

## Slide 5
Chart: 2100 Equilibrium Temperature Increase From Pre-industrial Level For Five IPCC Scenario CO2 Projections
| 500 | 575 | 740 | 850 | 990
1.5 climate sensitivity | 0.86973 | 1.0794 | 1.4578 | 1.6657 | 1.8944
4.5 climate sensitivity | 2.6092 | 3.2381 | 4.3734 | 4.997 | 5.6831
Notes: OLLI summer 13 Class 3 workpaper, downloaded from http://www.ipcc-data.org/observ/ddc_co2.html (last updated June 20, 2013)

## Slide 6: What equilibrium temperature means: 740 ppm example
Transient temperature
  Temperature when concentration reaches 740 ppm
Equilibrium temperature
  Temperature when radiative forcing is zero at 740 ppm
  Thermal radiation plus reflected solar radiation equals incoming solar radiation

## Slide 7: Why the lag? Near-term answer: Feedbacks
Water vapor: near-instantaneous
Longer: years to decades
  Vegetation
  Snow and ice cover
  Carbon pools:
    Soils and permafrost
    Methane hydrates???

## Slide 8: Long-Term Answer
Time needed to achieve equilibrium between surface and deep ocean
Necessary for both CO2 and temperature

## Slide 9
Curves represent peak CO2 of 450, 550, 650, 750, 850 and 1200 ppm
Notes: Solomon, et al., Irreversible climate change due to carbon dioxide emissions, PNAS (February 2009)

## Slide 10
Transient T/equilibrium T ratio
Ratio of temperature to equilibrium temperature for peak CO2
Notes: Solomon, et al., Irreversible climate change due to carbon dioxide emissions, PNAS (February 2009)

## Slide 11: What’s Happening?
At millennial time scale, CO2 largely equilibrates between ocean (~80%) and atmosphere (~20%)
  Result: Radiative forcing reduced from peak
But oceans gradually warm
  Result: reduced transfer of heat to ocean
Net result: near-constant temperature over millennium

## Slide 12: What does 1000 years mean?
1000 years ago
  William the Conqueror not yet born
  Spanish Reconquista just beginning
Irreversibility
  Not technically irreversible: geological cycle
  Irreversible in human terms
Possible escapes
  Net removal of CO2 from atmosphere
  Radiation management

## Slide 13: Doing something

## Slide 14: The Basic Alternatives
Reduce harm
Mitigation
Adaptation

## Slide 15: Mitigation Alternatives: Planet Keeling
Stabilize temperatures
  Stabilize atmospheric CO2:
    Emissions must not exceed absorption
    Natural and anthropogenic on both sides of balance
  Offset increasing greenhouse effect with increasing albedo: geoengineering
Undo warming
  Same tools
  Must achieve negative radiative forcing

## Slide 16: What Actions?
Mitigation
Reduce net CO2eq emissions
Radiation management

## Slide 17: What Actions?
Radiation management
Small scale: white roofs
Large scale: geoengineering

## Slide 18: Geoengineering
Leading candidate: inject sulfate aerosols into stratosphere
  Like continuous volcanic eruptions
Advantages
  Relatively cheap
  Only known alternative to:
    Reduce global temperatures on human time scale
    Quickly stabilize global temperature
Problems
  Stabilizes global average temperate
  Sole reliance creates growing temperature overhang
  Unknowns

## Slide 19: What Actions?
Reduce net CO2eq emissions
Capture and store emissions
Reduce energy-related CO2 emissions
Reduce non-energy CO2 emissions
Reduce other GHG emissions

## Slide 20: What Actions?
Reduce energy-related CO2 emissions
Reduce carbon intensity
Reduce energy intensity

## Slide 21: Classifying Determinants of Energy-Related CO2 Emissions
Energy intensity: (Energy consumed)/(value of output), e.g., Gigajoules/$$
Carbon intensity: (Carbon emissions)/(energy consumed), e.g., (Kg of CO2)/GJ

## Slide 22: Example: Plug-In Electric Vehicles
Energy intensity
  Energy consumed in generating electricity to move vehicle one mile
  Reduced by more efficient generation or vehicle
Carbon intensity
  How is the electricity generated
  Reduced by replacing fossil fuels with nuclear or renewables or replacing coal with natural gas

## Slide 23: What Actions?
Reduce carbon intensity
Expand renewables
Replace coal with natural gas
Expand nuclear power

## Slide 24: Jim Hansen and Nuclear Power
“Can renewable energies provide all of society’s energy needs in the foreseeable future? It is conceivable in a few places, such as New Zealand and Norway. But suggesting that renewables will let us phase rapidly off fossil fuels in the United States, China, India, or the world as a whole is almost the equivalent of believing in the Easter Bunny and Tooth Fairy.”
http://www.youtube.com/watch?v=CZExWtXAZ7M

## Slide 25: Expanding Renewables
The easy part: massive increase in electricity generated by solar and wind
The hard part: providing
  Round-the-clock electricity
  Energy for mobile sources

## Slide 26: Providing 24/7 Electricity
“Solar (or wind) is cheaper than nuclear” – doesn’t address the issue
Alternatives
  Wind and solar plus energy storage
  Fossil fuels plus carbon capture and storage
  Nuclear power
Issues:
  Technical feasibility within the chosen time frame
  Comparative economic cost
  Environmental impacts

## Slide 27: The International Dimension
OECD: most atmospheric CO2 inventory
Non-OECD: largest and growing share of current emissions
Standard of living – energy – CO2 link

## Slide 28
Notes: Earth Policy Institute, July 23, 2013

## Slide 29
Notes: Earth Policy Institute, July 23, 2013

## Slide 30
Notes: Earth Policy Institute, July 23, 2013

## Slide 31: United states

## Slide 32: U.S. Compared with. World
CO2
  More important: 85% vs. 77%
  Larger share from fossil fuels
    Land use changes not a net source
    Cement production less important
Methane (CH4) and nitrous oxide
  Less important – linked to agriculture’s smaller role
The moral: For US, primary focus on fossil fuels

## Slide 33: 2011 Share of Primary Energy
Chart: 
| Liquid fuels | Natural gas | Coal | Nuclear | Hydro | Biomass | Other renewables
 | 0.38032 | 0.25591 | 0.20197 | 0.084857 | 0.032566 | 0.028149 | 0.016232

## Slide 34: 2011 Share of Generating Capacity
Chart: 
| Coal | Natural gas & oil | Nuclear | Hydro | Wind | Other RN
 | 0.31294 | 0.44502 | 0.10063 | 0.077837 | 0.045677 | 0.017896

## Slide 35: 2011 Share of Generation
Chart: 
| Coal | Petroleum | Natural gas | Nuclear | Hydro | Wind | Other RN
 | 0.41516 | 0.0067194 | 0.23998 | 0.21238 | 0.078 | 0.028776 | 0.018987

## Slide 36: Points To Note
Renewable sources’ importance in economy and in electricity
Technologies’ shares of capacity and generation
Petroleum’s tiny role: price determined by superiority as transportation fuel

## Slide 37: Capacity Share vs. Generation Share
Chart: 
| Coal | Natural gas & oil | Nuclear | Hydro | Wind | Other RN
 | 0.31294 | 0.44502 | 0.10063 | 0.077837 | 0.045677 | 0.017896
Chart: 
| Coal | Petroleum | Natural gas | Nuclear | Hydro | Wind | Other RN
 | 0.41516 | 0.0067194 | 0.23998 | 0.21238 | 0.078 | 0.028776 | 0.018987

## Slide 38: 2006-2011 Growth
 | Billions of kWh | Annual growth rate
Total generation | 42.00 | 0.2%
RN generation | 150.16 | 7.0%
Hydro | 39.26 | 2.6%
Wind | 94.02 | 35.9%
PV | 5.24 | 66.8%

## Slide 39
Chart: US GHG Emissions 2010: Gigatons
| Fossil fuel combustion | Other CO2 | Methane | N2O | HFCs | Other
 | 5387.8 | 318.7 | 666.5 | 306.2 | 123 | 16.8
Notes: Class 1 workpaper

## Slide 40
Chart: Energy-Related 2011 CO2 Emissions
| Electricity | Non-electric transportation | Non-electric industrial | Non-electric commercial | Non-electric residential
 | 2240 | 1802 | 973 | 232 | 550
Notes: Source: 2010 AER

## Slide 41: Electricity Generation vs. Emissions
Chart: Energy-Related 2011 CO2 Emissions
| Electricity | Non-electric transportation | Non-electric industrial | Non-electric commercial | Non-electric residential
 | 2240 | 1802 | 973 | 232 | 550
Chart: 
| Coal | Petroleum | Natural gas | Nuclear | Hydro | Wind | Other RN
 | 0.41516 | 0.0067194 | 0.23998 | 0.21238 | 0.078 | 0.028776 | 0.018987

## Slide 42
Chart: US CO2 Emissions by Sector and Fuel
| Residential | Commercial | Industrial | Transportation | Electricity
Petroleum | 78.4675 | 39.2685 | 366.3982 | 1823.6595 | 35.0008
Natural gas | 260.0268 | 168.6449 | 412.2056 | 37.0795 | 408.1078
Coal | 0.65322 | 5.5617 | 148.6467 | 0 | 1842.974
Electricity | 892.1774 | 827.117 | 574.5899 | 4.1885 | 11.99
Primary Energy: coal, natural gas, petroleum
Energy carrier: electricity

## Slide 43: electricity as a solution

## Slide 44: Climate Policy Goal
Stable temperature needs stable GHG concentration
Stable concentration needs zero net emissions
Problem: Reconcile goal with modern energy services
Zero/near-zero net emission alternatives
  Renewables
  Nuclear
  Fossil fuels with CCS

## Slide 45: The Electrification Imperative
Alternatives ill-suited for directly supplying energy services
Require an intermediate energy carrier
  Electricity
  Hydrogen
Implication: Near-zero net emissions requires delivery of most energy in form of electricity

## Slide 46: Direct Use of Non-Carbon Energy
Primary Energy | Electricity Generation | Transportation | Thermal
Hydro | X |  | 
Wind | X |  | 
Biomass | X |  | X
Biofuels | X | X | X
Solar thermal | X |  | X
Solar PV | X |  | 
Geothermal | X |  | X
Nuclear | X |  | 
Carbon capture & storage | X |  | 

## Slide 47: Electricity: The Universal Energy Carrier
Fossil fuels
Nuclear
Renewables
Electricity
End use function
End use function
End use function

## Slide 48: How We Receive Energy Today
Chart: Delivered Energy Use & Electricity-Related Losses
| Petroleum | Natural Gas | Coal | Renewables | Delivered Electricity | Electricity-Related Losses | Total
Residential | 1.25 | 4.5 | 0.01 | 0.41 | 4.61 | 10.04 | 20.82
Commercial | 0.68 | 2.92 | 0.08 | 0.13 | 4.43 | 9.66 | 17.91
Industrial | 9.92 | 7.85 | 1.92 | 1.99 | 3.42 | 7.45 | 32.55
Transportation | 27.57 | 0.61 | 0 | 0 | 0.02 | 0.05 | 28.25
The Big Three
Notes: From AEO 2008

## Slide 49: Two Changes to Stabilize Temperatures
Chart: Delivered Energy Use & Electricity-Related Losses
| Petroleum | Natural Gas | Coal | Renewables | Delivered Electricity | Electricity-Related Losses | Total
Residential | 1.25 | 4.5 | 0.01 | 0.41 | 4.61 | 10.04 | 20.82
Commercial | 0.68 | 2.92 | 0.08 | 0.13 | 4.43 | 9.66 | 17.91
Industrial | 9.92 | 7.85 | 1.92 | 1.99 | 3.42 | 7.45 | 32.55
Transportation | 27.57 | 0.61 | 0 | 0 | 0.02 | 0.05 | 28.25
Notes: From AEO 2008

## Slide 50: Biomass
Often efficient for space heating
Limited alternative for electricity generation
Alternative for transportation
  Biofuels vs. EVs/fuel cells with non-CO2 electricity
  Liquid fuel vs. batteries or on-board hydrogen
  Need biofuels that don’t compete with food: cellulosic ethanol and algae-based fuel